## Slide 1
Raul CARREIRA RUFATO
Tutor Dr Joseph Morlier
Avoid aeroelasticity instabilities with a morphing airfoil by reinforcement learning

## Slide 2
Introduction
Morphing airfoils
Objective: avoid flutter, LCO and divergency
Approach: reinforcement learning
Aeroelastic instabilities

## Slide 3
Introduction
References
[1] Reinforcement Learning of Morphing Airfoils with Aerodynamic and Structural Eﬀects; Amanda Lampton,
Adam Niksch and John Valasek; AIAA 2007, Rohnert Park, California.
[2] Evaluating the impact of morphing technologies on aircraft performance; Jason Bowman, Major Brian
Sanders, Dr. Terrence Weisshaar; 43rd AIAA/ASME/ASCE/AHS/ASC 2002, Denver, Colorado
[3] Fundamentals of Aerodynamics; John D. Anderson, Jr.; McGraw-Hill Book Company, 1984
[4] Fluid-Structure Interactions: Volume 2; Paidoussis, Michael P.; Elsevier Science, 2016
[5] J. S. Gray, J. T. Hwang, J. R. R. A. Martins, K. T. Moore, and B. A. Naylor, “OpenMDAO: An Open-Source
Framework for Multidisciplinary Design, Analysis, and Optimization,” Structural and Multidisciplinary
Optimization, 2019.

## Slide 4
Subject
Module
Aerodynamics
Hypothesis
Incompressible flow
2D
Quasi-static aerodyn
Inviscid flow
Structure
Hypothesis
Linear deformations
2D
Quase-static
2 modes aproximation
Aero Loads
Interface
Loads to structural mesh
Struct Velocities & Displacements
Velocities & Displacements to fluid mesh
Calculus
Transfer loads between meshes
Verify aeroelastic instablities
Morphing airfoil shape (variation in chord and thickness)
Start
Flight conditions

## Slide 5
Subject
Big picture
Module
Start
No
Aerodynamics
Structure
Interface
Convergence?
Flight conditions
New airfoil
Optimum airfoil for flight conditions
Yes
[1] Reinforcement Learning of Morphing Airfoils
with Aerodynamic and Structural Eﬀects;
Amanda Lampton, Adam Niksch and John
Valasek; AIAA 2007, Rohnert Park, California.
[1], [2],[3]
[2] Fundamentals of Aerodynamics; John D.
Anderson, Jr.; McGraw-Hill B. Company, 1984
[3] J. S. Gray, J. T. Hwang, J. R. R. A. Martins, K. T.
Moore, and B. A. Naylor, “OpenMDAO: An
Open-Source Framework for Multidisciplinary
Design, Analysis, and Optimization,” Structural
and Multidisciplinary Optimization, 2019.
[3]
[1],[3],[4],[5]
[4] Fluid-Structure Interactions: Volume 2;
Paidoussis, Michael P.; Elsevier Science, 2016
[5] Reinforcement Learning: An Introduction,
Richard S. Sutton and Andrew G. Barto;
The MIT Press Cambridge, 2 edition, 2018

## Slide 6
Methodology
Develop aerodynamics and structure modules based on and [1];
Build a learning database for aeroelasticity (changing geometric parameters);
Add the wingbox in the Airfoil;
Change the airfoil parameter & the wingbox parameters to build a learning database;
Implement reinforcement learning method.
Validation of th aerodynamic model for an airfoil [1]
Reinforcement learning succes [1]

## Slide 7
Current work
Aerodynamics and structure modules
Building database changing geometrical parameters;

## Slide 8
Conclusions
Final thoughts and future work
Simplified model
Great applicability
More complex than expected
Future work
Finish the aeroelastic model
Implement reinforcement learning method to avoid aeroelastic instabilities (the simplest ones)
Expect everything right!!
Distant future: 3D approach and highly flexible wings

## Slide 9
Conclusions
Thank you for your attention!
Questions??